## Slide 1: Computer Organization and Assembly Language Lecture 8
Dr. Shafina

## Slide 2: Agenda
Today’s topics:
  Software
  Translating a Program
  Compiler
  Assembler
  Linker

## Slide 3: Software in a Computer
Application software
Programs user
writes and runs
Hardware
Systems software
Operating system
Compiler assembler
User

## Slide 4: Software
Application software,
a program in C:
swap (int v[ ], int k)
{int temp;
temp = v[k];
v[k] = v[k+1];
v[k+1] = temp;
}
MIPS binary machine code:
00000000101000010000000000011000
00000000000110000001100000100001
10001100011000100000000000000000
10001100111100100000000000000100
10101100111100100000000000000000
10101100011000100000000000000100
00000011111000000000000000001000
Compiler
Assembler
Application software
Hardware
Systems software
See pages 149-150
MIPS compiler output,
assembly language program:
swap;
muli $2, $5, 4
add $2, $4, $2
lw $15, 0 ($2)
lw $16, 4 ($2)
sw $16, 0 ($2)
sw $15, 4 ($2)
jr $31

## Slide 5: Our First Example
Now figure out the code:
swap(int v[], int k);
{ int temp;
temp = v[k]
v[k] = v[k+1];
v[k+1] = temp;
}
swap:
sll $2, $5, 2
add $2, $4, $2
lw $15, 0($2)
lw $16, 4($2)
sw $16, 0($2)
sw $15, 4($2)
jr $31

## Slide 6: Memory and Registers
Word 0
Word 1
Word 2
Word n
0
4
8
12
.
4n
.
.
.
.
.
Word n+1
Register 0
Register 1
Register 2
Register 3
Register 4
Register 31
Register 5
Memory
byte addr.
jump addr.
zero
.
.
.

## Slide 7: Policy of Register Usage (Conventions)
Register 1 ($at) reserved for assembler, 26-27 for operating system
2004 © Morgan Kaufman Publishers

## Slide 8: Translating a Program to Executable Code
C Program
(Data)
Compiler
(Sys. Prog.)
Assembly Language
Code (Data)
Assembler
(Sys. Prog.)
Machine Language
Object Code (Data)
Subroutine Library
Machine Language
Object Code (Data)
Linker
(Sys. Prog.)
Machine Language
Executable Code (Data)
Loader
(Sys. Prog.)
Program in
Computer
Memory

## Slide 9: Compiler
System program
Inputs:
    Programming language code, e.g., a C program
    Instruction set (including pseudoinstructions)
    Memory and register organization
Output: Assembly language code
Compiler’s function
    Specific to ISA and machine organization
    Assigns variables to registers
    Translates C into assembly language
    Saves and restores registers $s0 through $s7 when compiling a subroutine (or procedure) that uses them

## Slide 10: Compiler is a Multi-Pass Program
Programming language specific,
machine-independent processing
High-level optimization
(loop transformation, procedure
integration)
Global optimization
(register allocation, code
optimization)
Code generator
C or Java
Code
MIPS
Code
Decreasing program dependence
Increasing machine dependence
Intermediate representation

## Slide 11: Compiler Optimizes Code
Minimize number of machine instructions
    Example: x[i] = x[i] + 4, memory address for x[i] is generated only once, saved in a register, and used by lw and sw – Common subexpression elimination.
    Local optimization within a block of code.
    Global optimization across blocks.
    Global register allocation.
Strength reduction. Example: replace integer multiply by 2k with shift left.
Unnecessary instructions. A value not used in the later part of program may not be stored in memory (eliminate sw).

## Slide 12: MIPS Compiler Example
C code: f = (g+h) – (i+j)
Compiler assigns variables f, g, h, i and j to registers $s0, $s1, $s2, $s3 and $s4
Uses two temporary registers, $t0 and $t1, to produce the following MIPS assembly code:
add $t0, $s1, $s2 # reg $t0 contains g+h
add $t1, $s3, $s4 # reg $t1 contains i+j
sub $s0, $t0, $t1 # reg $s0 = $t0 – $t1
= (g+h) – (i+j)

## Slide 13: Registers $sp and $gp
0
pc
$gp
$sp
Stack
Dynamic data heap
Static data
Machine code (text)
Reserved
Temp. registers saved
before procedure call
$s0-$s7 saved in stack by
procedure
Global variables
in program

## Slide 14: Register $fp (Frame Pointer)
0
pc
$gp
$fp
Dynamic data heap
Static data
Machine code (text)
Reserved
$sp
Procedure frame
0
pc
$gp
$fp
Dynamic data heap
Static data
Machine code (text)
Reserved
$sp
Old procedure frame
Procedure frame

## Slide 15: Supporting procedures in computer hardware
In the execution of procedure, the program must follow these six steps:
  Put parameters in place where the procedure can access them
  Transfer control to the procedure
  Acquire the storage resources needed for the procedure
  Perform the desired task
  Put the result value in a place where the calling program can access them
  Return control to the point of origin, since a procedure can be called from several points in the program

## Slide 16: Compiling a Procedure Call
Consider a program that uses register $t0 and calls a procedure proc
Assembly code of program with procedure call:
.
.
addi $sp, $sp, - 4 # adjust stack pointer
sw $t0, 0($sp) # save $t0
jal proc # call proc
lw $t0, 0($sp) # restore $t0
addi $sp, $sp, 4 # pop 1 word off stack
.
.

## Slide 17: Assembler
System program
Input: Assembly language code
Output: Machine language code (binary or object code) contains:
  Machine instructions
  Data
  Symbol table
Converts pseudoinstructions into core instructions using register $at
Converts assembly code into machine code
Creates a symbol table – labels and locations in code

## Slide 18: MIPS Assembler Example
Use register convention:
  Registers 16-23 are $s0 through $s7
  Registers 8-15 are $t0 through $t7
Machine code: three 32-bit words from assembly code of slide 10
add 000000 10001 10010 01000 00000 100000
add 000000 10011 10100 01001 00000 100000
sub 000000 01000 01001 10000 00000 100010

## Slide 19: Assembler and Linker
Assembler
Assembler
Assembler
Main
Proc A
Proc B
Object file
Object file
Object file
Linker
Program
Library
Executable
File
Assembly
code
Machine code
(binary)
(binary)
(binary)

## Slide 20: Linker
System program.
Inputs: Program and procedure libraries, all in machine code.
Output: Executable machine code.
Linker functions:
  Links the machine code of procedures from a library.
  Sets memory addresses of data variables for procedures.
  Sets procedure addresses in the calling program code.

## Slide 21: Loader
System program
Inputs: Machine code and data from disc
Output: Set up program and data in memory
Loader functions:
  Read executable code and data from disc to computer memory
  Initialize registers and set stack pointer to first free location
  Transfer control to a start-up routine that calls the main routine of the program

## Slide 22: Recursive and Nested Programs
The following convention is understood and used by all calling (caller) and called (callee) programs.
Preserved Not preserved
Saved reg. $s0 - $s7 Temp. reg. $t0 - $t9
Stack pointer reg. $sp Argument reg. $a0 - $a3
Return addr. Reg. $ra Return value reg. $v0 - $v1
Stack above the stack pointer Stack below the stack pointer

## Slide 23: When Calee becomes a Caller
Saving and restoring of saved and temporary registers is done same as described before.
May reuse argument registers ($a0 - $a3); they are saved and restored as necessary.
Must reuse $ra; its content is saved in memory and restored on return.

## Slide 24: Example: Program→Callee A→Calee B
Main program Procedure A Procedure B
.
.
addi $a0, $zero, 3
jal A
.
.
.
.
addi $sp, $sp, -8
sw $ra, 4($sp)
sw $a0, 0($sp)
addi $a0, $zero, 7
jal B
lw $a0, 0($sp)
lw $ra, 4($sp)
addi $sp, $sp, 8
.
.
jr $ra
.
.
.
jr $ra

## Slide 25: Example: A Recursive Procedure
Int fact (n)
{
if (n < 1) return (1);
else return (n * fact (n-1));
}
This procedure returns factorial of integer n, i.e.,
n! = n × (n-1) × (n-2) × . . . × 2 × 1 = n × (n-1)!
Boundary case, 0! = 1

## Slide 26: Flowchart of fact
n < 1
v(n) = 1
n ≥ 0
v(n) = n * v(n-1)
Yes
No
Return v(n)

## Slide 27: Example: Compute 4!
n = 4
v(4) = 4 * v(3)
v(3) = 3 * v(2)
v(2) = 2 * v(1)
v(1) = 1 * v(0)
v(0) = 1
Main program calls fact, $a0 = 4
fact calls fact, $a0 = 3
fact calls fact, $a0 = 2
fact calls fact, $a0 = 1
fact calls fact, $a0 = 0
Returns $v0 = $v0 * $a0 = 24
Returns $v0 = $v0 * $a0 = 6
Returns $v0 = $v0 * $a0 = 2
Returns $v0 = $v0 * $a0 = 1
Returns $v0 = 1

## Slide 28: What to Save?
Recursive procedure will call itself. So,
  will reuse return address register $ra
  will change argument register $a0
These two registers must be saved.

## Slide 29: Saved Registers for 4! Example
Initial $sp
$sp
fact calls fact, $a0 = 3
fact calls fact, $a0 = 2
fact calls fact, $a0 = 1
fact calls fact, $a0 = 0
Return address within main program
Argument register, $a0 = 4
Return address within fact
Argument register, $a0 = 3
Return address within fact
Argument register, $a0 = 2
Return address within fact
Argument register, $a0 = 1
}
}
}
}

## Slide 30: Assembly Code for fact
fact:
addi $sp, $sp, -8 # adjust stack for two items
sw $ra, 4($sp) # save return address of caller
sw $a0, 0($sp) # save caller supplied argument n
slti $t0, $a0, 1 # $t0 = 1, if n ≤ 1, i.e., n = 0
beq $t0, $zero, L1 # go to L1, if n ≥ 1
addi $v0, $zero, 1 # return $v0 = 1 to caller
addi $sp, $sp, 8 # no need to restore registers, since
none was changed, but must
restore stack pointer
jr $ra # return to caller instruction after jal

## Slide 31: Assembly Code Continued
L1: addi $a0, $a0, -1 # set $a0 to n-1
jal fact # call fact with argument n-1
lw $a0, 0($sp) # on return from fact, restore n
lw $ra, 4($sp) # restore return address
addi $sp, $sp, 8 # adjust stack pointer
mul $v0, $a0, $v0 # n! = n × (n-1)!
jr $ra # return to caller

## Slide 32: Summary
A user’s program is processed by several system programs:
  Compiler
  Assembler
  Linker
  Loader
  Start-up routine: begins program execution and at the end of the program issues an exit system call.