## Slide 1: Computer Organization and Assembly Language Lecture 7
Dr. Shafina

## Slide 2: Agenda
Today’s topics:
  Datapath and Control

## Slide 3: Von Neumann Kitchen
Registers
ALU
Control
Memory
Output
Program
Data
My choice
PC
Start
Processor
Input

## Slide 4: Where Does It All Begin?
In a register called program counter (PC).
PC contains the memory address of the next instruction to be executed.
In the beginning, PC contains the address of the memory location where the program begins.

## Slide 5: Where is the Program?
Machine code
of program
Memory
Start
address
Program counter
(register)
Processor

## Slide 6: How Does It Run?
Start
PC has memory address where program begins
Fetch instruction word from memory address in PC
and increment PC ← PC + 4 to point to next instruction
Decode instruction
Program
complete?
Yes
No
STOP
Execute instruction
Save result in register or memory

## Slide 7: Datapath and Control
Datapath: Memory, registers, adders, ALU, and communication buses. Each step (fetch, decode, execute, save result) requires communication (data transfer) paths between memory, registers and ALU.
Control: Datapath for each step is set up by control signals that set up dataflow directions on communication buses and select ALU and memory functions. Control signals are generated by a control unit consisting of one or more finite-state machines.

## Slide 8: Datapath for Instruction Fetch
PC
Instruction
Memory
4
Address
Instruction
word to
control unit
and registers
Add

## Slide 9: Register File: A Datapath Component
32 Registers
(reg. file)
Write
register
reg 1 data
reg 2 data
5
5
5
32
32
32
reg 1
reg 2
Read
registers
Write data
RegWrite
from control

## Slide 10: Multi-Operation ALU
ALU
3
zero
result
overflow
Operation
select
from control
Operation select ALU function
000 AND
001 OR
010 Add
110 Subtract
111 Set on less than
zero = 1, when all bits of result are 0

## Slide 11: R-Type Instructions
Also known as arithmetic-logical instructions
add, sub, slt
Example: add $t0, $s1, $s2
  Machine instruction word
  000000 10001 10010 01000 00000 100000
  opcode $s1 $s2 $t0 function
  Read two registers
  Write one register
  Opcode and function code go to control unit that generates RegWrite and ALU operation code.

## Slide 12: Datapath for R-Type Instruction
32 Registers
(reg. file)
Write reg.
number
5
5
5
32
32
$s1
$s2
Read
register
numbers
Write data
ALU
3
zero
result
overflow
Operation
select
from control (add)
10001
10010
01000
RegWrite
from control
activated
32
$t0
  000000 10001 10010 01000 00000 100000 opcode s1 $s2 $t0 function (add)

## Slide 13: Load and Store Instructions
I-type instructions
lw $t0, 1200 ($t1) # incr. in bytes
100011 01001 01000 0000 0100 1011 0000
opcode $t1 $t0 1200
sw $t0, 1200 ($t1) # incr. in bytes
101011 01001 01000 0000 0100 1011 0000
opcode $t1 $t0 1200

## Slide 14: Datapath for lw Instruction
Operation
select
from control
(add)
32 Registers
(reg. file)
Write reg.
number
5
5
5
32
32
$t1
Read
register
numbers
Write data
ALU
3
zero
result
overflow
01001
01000
RegWrite
from control
activated
32
Sign
extend
16
0000 0100 1011 0000
Data
memory
Addr.
Read
data
MemWrite
MemRead
activated
$t0
Write
data
100011 01001 01000 0000 0100 1011 0000
opcode $t1 $t0 1200
mem. data to $t0

## Slide 15: Datapath for sw Instruction
Operation
select
from control
(add)
32 Registers
(reg. file)
Write reg.
number
5
5
5
32
32
$t1
$t0
Read
register
numbers
Write data
ALU
3
zero
result
overflow
01001
RegWrite
from control
32
Sign
extend
16
0000 0100 1011 0000
Data
memory
Addr.
Read
data
$t0 data to mem.
01000
MemWrite
activated
MemRead
Write
data
101011 01001 01000 0000 0100 1011 0000
opcode $t1 $t0 1200
32

## Slide 16: Branch Instruction (I-Type)
beq $s1, $s2, 25 # if $s1 = $s2, advance PC through 25 instructions
16-bits
000100 10001 10010 0000 0000 0001 1001
opcode $s1 $s2 25
Note: Can branch within ± 215 words from the current instruction
address in PC.

## Slide 17: Datapath for beq Instruction
Operation
select
from control (subtract)
32 Registers
(reg. file)
Write reg.
number
5
5
5
32
32
$s1
Read
register
numbers
Write data
ALU
3
zero
result
overflow
10001
10010
RegWrite
from control
32
Sign
extend
16
0000 0000 0001 1001
Shift
left 2
Add
16-bits
000100 10001 10010 0000 0000 0001 1001
opcode $s1 $s2 25
$s2
32
32
32
To branch
control
logic
PC+4
From instruction
fetch datapath
Branch
target
32

## Slide 18: Assignment # 2
Draw Data paths for R-type, I-type and Branch Instructions